## Slide 1: Cheap & Simple Transverters New and Updates
Paul Wade W1GHZ

## Slide 2: Cheap & Simple Transverters
2304-3456 Transverter Update
1296 Transverter Update
902 Transverter Update
Universal MMIC Preamp
432 Transverter – NEW
Smart & Fool-Resistant Conditional Sequencer – Mark 4

## Slide 3: 2304-3456 MHz Transverter Update
New MMICs –
  Higher gain and power
  Lower Noise Figure
  New footprint – SOT-89 package

## Slide 4: 2304 Transverter

## Slide 5: 2304-3456 Transverter Schematic

## Slide 6: 2304 MHz Performance
Noise Figure ~ 5 dB
  Needs Preamp
Power Output ~ +17 dBm (50 mW)
  Cheap WiFi booster – 2+ watts

## Slide 7: 1296 MHz Transverter Update
New MMICs –
  Higher gain and power
  Lower Noise Figure
  New footprint – SOT-89 package
Power splitter – Minicircuits

## Slide 8: PC board

## Slide 9: Power Splitter

## Slide 10: LO Multiplier PC board Mod

## Slide 11: 1296 Transverter Performance
Noise Figure ~ 8 dB
  Not enough gain
  Needs Preamp
Power output ~ +18 dBm at 1dB Comp.
  +20 dBm saturated

## Slide 12: 902 MHz Transverter
New MMICs –
  Higher gain and power
  Lower Noise Figure
  New footprint – SOT-89 package
Power splitter – Minicircuits
Soldermask
  Easier soldering
  Protect printed hairpin filter

## Slide 13: PC Board

## Slide 14: New TX MMICs

## Slide 15: RX MMIC and Splitter

## Slide 16: Printed Filter with Soldermask

## Slide 17: 902 Performance
Noise Figure ~ 4 dB
  (Lower filter loss than 1296 Transverter)
Power Output +18 dBm at 1 dB comp
  + 20 dBm saturated

## Slide 18: 1296 MHz Next Revision
Add RX second stage
  No space on board
Minicircuits VNA-25
  Separate voltage pin, no bias network
  High reverse isolation
Soldermask – easier assy, protect filter
Noise Figure now ~ 1.3 dB

## Slide 20: Universal MMIC Preamp
Low NF MMICs with no tuning
PGA-103 – SOT-89 package, < 1 dB NF
PSA4-5043 – SOT-343 package, < 1dB NF
PHA-1H -- < 2 dB NF, +40 dBm IP3
3 to 5 volt operation – no resistor needed

## Slide 21: Simple Schematic

## Slide 22: Old Preamp – Altoids tin

## Slide 23: Universal Preamp any MMIC package
PC pattern SOT-343 SOT-89 Micro-X

## Slide 24: Easy Assembly

## Slide 25: Fits in Pomona Box

## Slide 26: 432 MHz Transverter for SDR
Good IF for higher Microwaves
Find signals in contests
Higher dynamic range
And my 432 Transceiver died before January contest

## Slide 27: Printed Combline Filter

## Slide 28: Component Tolerance
5% Tolerance is
never right on

## Slide 29: 432 Transverter – 3 Filters

## Slide 30: 432 Transverter Schematic

## Slide 31: Component choices
Many MMIC choices
  2 TX stages, 2 RX stages
  Comb filter between stages - stability
  Universal MMIC Footprint for RX front end
  LO amplifier
Minicircuits Mixer
  High-level +17 dBm for high IP3
  Standard +7 dBm for lower LO power

## Slide 32: Performance
Noise Figure under 1 dB
Power output > +20 dBm at 1dB comp.
Drive Mitsubishi module for more power
RA30H4047M1 – 25 watts
RA07H4047M – 7 watts
  Enough for Solid-state PA
  400 watt ebay Amp < $100

## Slide 33: Prototype in Tin Box

## Slide 34: W1FKF Version

## Slide 35: A Smart and Fool-Resistant Conditional Sequencer
Paul Wade
W1GHZ

## Slide 36: Why a Sequencer?
Protect Preamp
Protect Coax Relay
Protect Power Amp
Often includes IF interface
  Reduce IF Transceiver power

## Slide 37: Mark 4 Sequencer
Still trying to design a Fool-Proof Sequencer
For 20 years
And still make it cheap and easy to build ( one in each transverter)

## Slide 38: Coax Relay
ON
  High Power
  High Isolation
SWITCHING
  Low Power
  Low Isolation
  Easily damaged

## Slide 39: Waveguide Switches
High Power and Isolation
but NOT while switching

## Slide 40: Why Fool-Resistant? Why not Fool-Proof?
Because there is always a bigger fool!
Only a fool wouldn’t use a sequencer

## Slide 41: Transverter sans Smoke

## Slide 42: Basic Sequencer
Detect PTT
Switch Coax Relay
Turn on Power Amp
Just time delays – like clockwork
  Ready or not

## Slide 43: Fool-Resistant Sequencer
Detect PTT or sense RF
Inhibit Transmit – dump IF power
Disable RX
Switch TR relay
  Check AUX contacts
Power to PA
  Check for PA ready
Enable Transmit

## Slide 44: Conditional Sequencer
Not just time delay clockwork
Conditions before next state
  TR relay external contacts
  Power Amplifier Ready
  Additional conditions as needed
Graceful exit if PTT dropped

## Slide 45: Sequencer Timing

## Slide 46: Original Fool-Resistant Sequencer (1997)

## Slide 47: Replaced W1VT IF Interface

## Slide 48: Original Fool-Resistant Sequencer
Lessons
  Don’t pick box first
  Tight construction
  Difficult to build, harder to fix or modify
  CMOS logic for RC timing = poor predictability
  Need connectors for External Connections

## Slide 49: Simple Fool-Resistant Sequencer

## Slide 50: Simple Fool-Resistant Sequencer Mark 2 (2003)
Small and simple – minimal IF interface
For transverters with some internal switching and power reduction (DB6NT)
Very popular

## Slide 51: Even More Fool-Resistant Sequencer (2009) – Mark 3

## Slide 52: Technology
Readily available and cheap
  Around for 20 years
  Will be for another 20 years
  Comparators
  Resistors
  Capacitors
  PIN diodes
  Opto-isolators
PC Board with Silk-screen Identifiers
Many parts – tedious to build

## Slide 53: PC Board
Full Silkscreen for Easy Assembly

## Slide 54: Flexibility
PTT high or low, thru coax if desired
RF sense for Fail-Safe, switching if desired
PIN diode IF switch – 100 mw to 10W+ IF
TR relay active on TX or on RX
Option for bidirectional amplifier
External connections thru opto-isolators
Customize with X-Acto knife

## Slide 55: PIN diode Switch
Between IF rig and Transverter
Three states
  RX – MMIC amp to recover losses
  Fail-Safe – Absorbs all power until sequence complete
  TX – enables drive to transverter
TX Power Adjustable
Separable, could be omitted

## Slide 56: Fail-Safe
PTT or Inhibit line can Fail
  I run PTT on IF coax
RF Sense detects any RF from XCVR
PIN switch disables RX, absorbs RF
Cheap MMIC amp protects mixer (fuse)
Option – TX with RF sense

## Slide 57: PIN diode Switch

## Slide 58: Opto-isolator
All external connections isolated
Several KV isolation possible
Requires 2-wire connections (no common ground) for real isolation
Connections could be remote

## Slide 59: Does It Work?
Flawlessly in 10 GHz Contest

## Slide 60: Why no Microprocessor? (in Mark 3)
How soon will chip be obsolete?
  Many competing processor choices
Will the software be bug-free?
Who will program chips?
Need programming to make changes
Microprocessor in RF environment?

## Slide 61: Mark 4 – with Arduino
Many small Microprocessors available
Arduino is simple, cheap, and ubiquitous
Easy to load and change software – USB
Good software environment
Book by W8TEE and W6DQ:
Arduino Projects for Amateur Radio

## Slide 62: Sequencer Mark 4 Hardware
Same IF interface as Mark 3 with Fail-safe PIN diode switch (without wires)
  Separate RX Disable from TX Enable
Separable RX and TX both sides
All control by Arduino
Power FETs for external drivers
  Arduino can’t drive relays or 12+ volts

## Slide 63: IF interface plus Arduino

## Slide 64: IF PIN Switch Arduino control

## Slide 65: Arduino
Adafruit Pro Trinket
Simple Module
USB connector
Plenty of IO pins
Analog inputs (voltage)
Adequate memory
3.3 & 5 volt versions
$10
Plugs into PCB

## Slide 66: IF interface – PIN diode switch RF on the PC backside

## Slide 67: Everything else is software
Sequencer is as complex as you want
Flexible, easily changed
Add or change sequence states
Run slowly to Debug, watch LEDs
My version takes 2K of memory, 28K available
Lots of room for other enhancements

## Slide 68: Sequencer - State Machine
Fail-Safe

## Slide 69: What else could Arduino do?
Inhibit Transceiver output
Load Synthesizer Frequency
VSWR monitor and shutdown
  analog inputs
• Amplifier voltage
• Temperature monitor (external sensor)
• TR relay auxiliary contacts
• Latching relay driver
• Multiband transmit protection (Rover)

## Slide 70: What else could Arduino do? - continued
Rotator control
Grid calculator from GPS output
Send CW
  Dash sender
  CW ID
  Call and grid string
  CW keyboard
Whatever you can think of

## Slide 71: Simple 1296 MHz Transverter

## Slide 72: 3456 MHz Lunchbox Transverter

## Slide 73: Summary
Full-Featured Sequencer
Flexible – your program
Easy to build
Readily available components
Inexpensive
And Fool-Resistant

## Slide 74: Version without PIN-diode IF interface SDR XVTR, Amplifier Control

## Slide 75: More Details
www.w1ghz.org
Arduino sketches (software)
Pictures, schematic, parts list, etc.
Boards are available