## Slide 1: 10 Band Rover Control Box
44th EASTERN VHF/UHF/MICROWAVE CONFERENCE
April 21, 2018
Bill Koch W2RMA
W2RMA@ARRL.NET

## Slide 2: Some have great locations….

## Slide 3: And some have to rove ….
N

## Slide 4: Why Be a Rover?
Ham radio + Outdoors
Meet people, camaraderie, sun  activate grids
You’re wanted – ‘/R’ brings you to top the pile!
Opportunity to sell technology - STEM
    Much more than Grandpa’s Ham Radio
Can start simply – and grow it through time
    1 - 4 bands – FM only or mixed modes
    5 + bands
Sound interesting?
    Rove with another ham
    Just DO IT!

## Slide 5
Perry Park, Lake Erie

## Slide 6: Sunset Lake Erie

## Slide 7: Why Be a Rover?
Ham radio + Outdoors
Meet people, camaraderie, sun  activate grids
You’re wanted – ‘/R’ brings you to top the pile!
Opportunity to sell technology - STEM
    Much more than Grandpa’s Ham Radio
Can start simply – and grow it through time
    1 - 4 bands – FM only or mixed modes
    5 + bands
Sound interesting?
    Talk with rovers
    Rove with another ham

## Slide 8: Simple & Effective Start – 4 bands
4 bands - VHF: 50, 144, 222, 432 – use what you have!
Antennas
    FM: verticals
    SSB/CW: Omni, Quad, MOXON, Quagi. Cheap!
Antenna Switch needed – UHF rotary works fine
    ‘Protect thy front end’
Can operate in motion – but safer to stop
    Distracted driving law restrictions
    Logging
If you have a V/UHF rig, you can rove!

## Slide 9: Considerations for ‘10 Bands’
What is my objective in 10 band roving? Outcomes desired?
Vehicle: Van / Truck / SUV / car
Playtime & Budget: 10 bands = 10 stations
Rig / Transverter acquisition: Builder vs operator
Power: RF & DC
Frequency accuracy / stability
Antennas: Mounting / type / pointing
Control system: ~5 signals – band, IF, LO, PTT, Feedback
K0BAK: ‘For rovers, everything is a compromise.’
  Beware of analysis – paralysis! Just DO IT!

## Slide 10: The Box

## Slide 11: Considerations: Building the Box
Passenger car. No roof rack nor hitch. 
Change bands quickly -- < 30 seconds : logging?
# bands: 10 less 144, 5760, 10368
Transverter/Power: W1GHZ boards; Pout: 50+ except $$$ bands
LNA protection: LNA = $$. Spend $ to protect.
Local oscillator: centralized A32 with Morion OCXO
  Accuracy / Stability -- SSB/CW vs. FT-8
IF rig (FT817) control: bands, frequencies, Pout
Sequencing: at the transverter. Feedback -> ‘done’
Logging / integration: I’net - sporadic coverage 
  N3FJP instead of N1MM, ON4KST
Reliability vs. complexity: Wires / computers complex

## Slide 12: Inside the Box
LO output
PTT, Band, FB
IF hidden below
Band switch
Logic boards
2 x 8P coax switch
12 -> 24 V booster
LO chain

## Slide 13: Considerations: The Box as Built Yellow = Done
Change bands quickly -- < 30 seconds : logging problem
# bands: 10 less 144, 5760, 10368
Transverter Power: 50+ except $$$ bands
LNA protection: LNA = $$
Local oscillator: generally centralized / few decentralized
  Accuracy – on frequency
  Stability: SSB/CW vs. FT8
IF rig (FT817) control: IF freqs, drive power: manually FT817
Sequencing: at the transverter. Feedback final step done.
Logging integration: internet - sporadic coverage
  N3FJP instead of N1MM, ON4KST  - Home stations: call CQ!
RELIABILITY vs. complexity: Switch & Wires / computers problematic
Built for change: can add a 7”x10” box third level

## Slide 14: Let’s Do It ….
Talk to a ham that roves. Look at the setup.
Accompany a rover.
Use your existing VHF/UHF rigs – 1 gets you started!
If you rove already, how about adding a band?
Search internet for ‘ham radio rover’. Lots of content.
  K0BAK, W1GHZ, K8GP, KA2LIM, N6NB, K0NR .…..
  ARRL contest rules. Sprints. MADs.
Roving is a journey, not a destination
  ALWAYS something to learn / improve
  10 bands is 91% of 11; 83% of 12 …..

## Slide 15: 73 & See ‘Yinz’ on VHF, 222UP & 10UP !
CT
BLOCK IS.
de FN00rg
&
W2RMA/R