## Slide 1
Why Not Go Roving?
Sean Waite, WA1TE
Presented to the 44th Eastern VHF/UHF/Microwave Conference
2018/04/21

## Slide 2
whoami
Licensed since 2012 as KB1YOQ, Extra since 2015 and became WA1TE
Trustee of the Signals, Summits, and Suds radio club callsign, K1SIG
Relatively new rover – a veteran of 2 September (2016, 2017) contests and 1 January contest (2018)

## Slide 3
What is a Rover?
“A rover consists of no more than two operators that moves among two or more grid squares during the course of a contest”
3 classes – Limited, Classic, Unlimited
Boatloads of fun
May work from 1 grid Saturday, 1 grid Sunday
May work 27 grids on a mammoth rove from PA to TX
Likely to be somewhere in between
  K1SIG/R 3 grids, 6 grids, 14 grids

## Slide 4
Why Does K1SIG Rove?
QTH in a hole
No towers/tall masts
Hard to make any real effort from compromised stations
Well...let’s give it a shot
Turns out, a load of fun
Operate from scenic locations
  Like Walmart parking lots
  Also mountain tops
Something to do during the slow times of the contest

## Slide 5
September Setup
ICOM IC-746, 100W on 2m
  7el M2 yagi
ICOM IC-7000, 100W on 6m
  PVC + wire 2 el moxon
Yaesu FT-790RII, 25W on 70cm
  15el Diamond yagi
RS HTX-100 + UR3LMZ xvrtr, ~6W on 1.25m
  10el DSE yagi
Yaesu FT2900RII @75W and Yaesu FT290RII @25W on 6m while mobile
Homebrew drive over mast mount
Hitch flagpole holder
2m, 1.25m and 70cm loops while mobile
2 masts while fixed – 10’ EMT conduit
2x 100Ah 12VDC AGM Deep Cycle Batteries

## Slide 6
January Setup

## Slide 9
January Setup
ICOM IC-7000 on 6/2/70 at 100W/50W/35W
HTX-100 with xvrtr on 1.25 at 6W
Yaesu FTM-100DR on 2m, 70cm FM
Alinco DR-235T on 1.25FM
Yaesu FT-290RII w/ SG-Lab Transverters on 903 and 1296
10’ PVC mast with loops (assorted brands)
2/70 short vertical
1.25m ¼ wave vertical
2el HB9CV beams on 903, 1296
Same batteries (overkill, but trying to wear level)

## Slide 12
Why Such Different Setups?
Stop and Shoot
Lots of time to work stations
Get up high, work long range
Long setup – don’t want to move much
Awkward to work from populated areas
Easier to split workload
Run and Gun
Good spots closed in Winter
Work more mults, vs longer contacts
Get in their face
Fast setup – can use full station while moving
Compact, easy to operate from parking lot

## Slide 13
Simple Rovers
Modest stations can be effective
  You don’t need long range capabilities if you can just drive in close
  Fixed stations are much more capable and will look for you
HF+6 rig and a loop or moxon
Dual band mobile
Focus on 6 and 2 – as loud as you can get here
2m FM is handy, though a bit quiet
  If it’s all you have, USE IT
  If you have 2m SSB/CW, bring the FM radio anyway

## Slide 15
Rover Power!
Don’t strand yourself
Car batteries do not like to be drained
12V Deep Cycle batteries
6V Deep Cycle batteries in series
  Handles high current a little better
Generators
  Useful, but annoying to those around you
  Longer operating time
  Heavy and take up space
Difficult to handle voltages other than 12V
Laptops are power hungry
28/24V devices might be hard
  Need boost converter or 2nd battery string (which you may not be able to charge)
4AWG jumper cables are cheap source of heavy gauge cable
Quick disconnects are useful to break battery string from car battery when car is off during operation
  K1SIG uses Anderson SB-120 connectors

## Slide 16
Always Improving
Look at what others are doing
  Getting caught late at night by your wife while staring at pictures of other rovers…
Read soapboxes
Ask for help!
What went well, what went poorly last time?
Keep notes
More bands are an easy way to add mults
  Unless you want to stay limited
  Modest setup can work well here as well
  May surprise you how far you can work with these
  Diminishing returns, watch who in your path have the bands you want to add

## Slide 17
Choosing Locations
Get up high
Get out in the open
Find the big stations and look for paths to them
Compact Rover? Parking lots!
Watch for RF Hell
  Mountain tops are full of cell, pager, radio towers
Careful of tempting grids where no one aims
  FN51
Have backup sites
  Other ops may already have “your” site

## Slide 18
Choosing Locations

## Slide 19
Spot, spot, spot
Spam the mailing lists with your plans
K1RZ/W3SZ database
Get phone numbers
  Some ops like calls, other SMS
Roverstatus app on android
APRS
Facebook, reddit, discord, twitter…
  Really, just be annoying
Fixed stations WILL look for you if the know you are out there

## Slide 20
Be Safe
Those batteries have a lot of juice and you are conductive
  So are your antennas, masts, cables…
  People weld with big batteries
  Sealed batteries are better – less venting of hydrogen gas or dumping out of acid in your car
Secure stuff in the car
  Keep it away from the batteries
  Keep it away from the driver
  Keep it from clobbering you if you experience a sudden deceleration (or roll...)
Take breaks!
  Tired drivers are no good
  Coffee keeps you awake...and mandates stretching of legs
Don’t park in unsafe spots
  Edge of highway
  Bronx park at 1am

## Slide 21
Be An Ambassador
You are more visible to the public than most fixed stations
You will get questions
  What is that stuff?
  Are you the NSA?
  Are you talking to the mother ship?
  Are you tracking birds?
  Are you nuts?
Be friendly
  Especially if the nice police officer actually had a reason to pull you over
Maybe consider bringing flyers
Signs on your car may be nice as well
Don’t park where you’re a nuisance
  If asked to move, just move

## Slide 22
Links
http://w3sz.x10.mx/k1rz/K1RZDataBaseInstructions.html
http://www.roverstatus.info/

## Slide 23
Thanks!
Any questions?